## Slide 1
GREENHOUSE SENTINEL
Greenhouse Sentinel Operator Training
A short practice deck for greenhouse volunteers
Notes: [Sources]
- training/jays-book.json — deck title, sequence, and training framing.

## Slide 2
Connect and Verify
• Place the hub above the irrigation line and away from direct spray.
• Connect both probes before applying power.
• Join the temporary network named sentinel-setup.
• Open http://sentinel.local and choose the greenhouse network.
• Select Run sensor check.
• A successful check reports all three readings and changes the hub indicator from amber to green.
2
Notes: [Sources]
- docs/product/quickstart.md#connect-and-verify — single-sourced from Katie's maintained product documentation.

## Slide 3
Daily Check
• Confirm the dashboard timestamp is less than two minutes old.
• Review the current state and its explanation.
• Compare soil moisture across the three most recent samples.
• Acknowledge any completed response.
• Record an observation only when local conditions differ from the sensor data.
3
Notes: [Sources]
- docs/product/operations.md#daily-check — single-sourced from Katie's maintained product documentation.

## Slide 4
Decision States
• The engine assigns one of three states after three consecutive samples meet the same condition.
• State — Example condition — Operator expectation
• Normal — All readings are inside target ranges — Continue scheduled checks
• Watch — One reading is near a threshold — Inspect within 30 minutes
• Act — One reading exceeds a threshold — Follow the displayed response
• The three-sample rule reduces noise without hiding sustained change. Thresholds in this demo are illustrative, not horticultural advice.
4
Notes: [Sources]
- docs/product/architecture.md#decision-states — single-sourced from Katie's maintained product documentation.

## Slide 5
Practice: choose the next action
• The dashboard shows Watch after three consecutive high-temperature samples.
• In pairs, identify the first inspection step and explain what you would record.
• Be ready to share one concise acknowledgement note.
5
Notes: [Sources]
- training/jays-book.json — Jay's training-only exercise; not copied from Katie's maintained product documentation.